## Slide 1: Digital signal processing
-G Ravi kishore

## Slide 2: INTRODUCTION
The goal of DSP is usually to measure, filter and/or compress continuous real-world analog signals.
The first step is usually to convert the signal from an analog to a digital form, by sampling and then digitizing it using an analog-to-digital converter (ADC), which turns the analog signal into a stream of numbers.
However, often, the required output signal is another analog output signal, which requires a digital-to-analog converter (DAC).
Even if this process is more complex than analog processing and has a discrete value range, the application of computational power to digital signal processing allows for many advantages over analog processing in many applications, such as error detection and correction in transmission as well as data compression.

## Slide 3: Signal sampling
To use an analog signal on a computer, it must be digitized with an analog-to-digital converter.
Sampling is usually carried out in two stages, discretization and quantization. In the discretization stage, the space of signals is partitioned into equivalence classes and quantization is carried out by replacing the signal with representative signal of the corresponding equivalence class.

## Slide 4: DSP DOMAINS
Time and space domains
The most common processing approach in the time or space domain is enhancement of the input signal through a method called filtering. Digital filtering generally consists of some linear transformation of a number of surrounding samples around the current sample of the input or output signal.

## Slide 5
A "linear" filter is a linear transformation of input samples; other filters are "non-linear". Linear filters satisfy the superposition condition, i.e. if an input is a weighted linear combination of different signals, the output is an equally weighted linear combination of the corresponding output signals.

## Slide 6
A "causal" filter uses only previous samples of the input or output signals; while a "non-causal" filter uses future input samples. A non-causal filter can usually be changed into a causal filter by adding a delay to it.
A "time-invariant" filter has constant properties over time; other filters such as adaptive filters change in time.
A "stable" filter produces an output that converges to a constant value with time, or remains bounded within a finite interval. An "unstable" filter can produce an output that grows without bounds, with bounded or even zero input.
A "finite impulse response" (FIR) filter uses only the input signals, while an "infinite impulse response" filter (IIR) uses both the input signal and previous samples of the output signal. FIR filters are always stable, while IIR filters may be unstable.

## Slide 7: Frequency domain
Signals are converted from time or space domain to the frequency domain usually through the Fourier transform. The Fourier transform converts the signal information to a magnitude and phase component of each frequency. Often the Fourier transform is converted to the power spectrum, which is the magnitude of each frequency component squared.
The most common purpose for analysis of signals in the frequency domain is analysis of signal properties. The engineer can study the spectrum to determine which frequencies are present in the input signal and which are missing.

## Slide 8: Z-plane analysis
Whereas analog filters are usually analysed in terms of transfer functions in the s plane using Laplace transforms, digital filters are analysed in the z plane in terms of Z-transforms.
A digital filter may be described in the z plane by its characteristic collection of zeroes and poles. The z plane provides a means for mapping digital frequency (samples/second) to real and imaginary z components, where for continuous periodic signals and ( is the digital frequency). This is useful for providing a visualization of the frequency response of a digital system or signal.

## Slide 9: Wavelet
In numerical analysis and functional analysis, a discrete wavelet transform (DWT) is any wavelet transform for which the wavelets are discretely sampled.
As with other wavelet transforms, a key advantage it has over Fourier transforms is temporal resolution: it captures both frequency and location information

## Slide 10: DSP- design requirements
Phase and group delay: An all-pass filter passes through all frequencies unchanged, but changes the phase of the signal. Filters of this type can be used to equalize the group delay of recursive filters. This filter is also used in phaser effects.
A Hilbert transformer is a specific all-pass filter that passes sinusoids with unchanged amplitude but shifts each sinusoid phase by ±90°.
A fractional delay filter is an all-pass that has a specified and constant group or phase delay for all frequencies.

## Slide 11
The impulse response
There is a direct correspondence between the filter's frequency function and its impulse response: the former is the Fourier transform of the latter. That means that any requirement on the frequency function is a requirement on the impulse response, and vice versa.
Causality
In order to be implementable, any time-dependent filter (operating in real time) must be causal: the filter response only depends on the current and past inputs. A standard approach is to leave this requirement until the final step.
Stability
A stable filter assures that every limited input signal produces a limited filter response. A filter which does not meet this requirement may in some situations prove useless or even harmful. Certain design approaches can guarantee stability, for example by using only feed-forward circuits such as an FIR filter. On the other hand, filter based on feedback circuits have other advantages and may therefore be preferred, even if this class of filters include unstable filters. In this case, the filters must be carefully designed in order to avoid instability.

## Slide 12
Locality
In certain applications we have to deal with signals which contain components which can be described as local phenomena, for example pulses or steps, which have certain time duration. A consequence of applying a filter to a signal is, in intuitive terms, that the duration of the local phenomena is extended by the width of the filter. This implies that it is sometimes important to keep the width of the filter's impulse response function as short as possible.
Computational complexity
A general desire in any design is that the number of operations (additions and multiplications) needed to compute the filter response is as low as possible. In certain applications, this desire is a strict requirement, for example due to limited computational resources, limited power resources, or limited time. The last limitation is typical in real-time applications.