## Slide 1
Chapter 3
VLSI Subsystem Design
Jin-Fu Li
Advanced Reliable Systems (ARES) Laboratory Department of Electrical Engineering
National Central University Jhongli, Taiwan

## Slide 2: Outline
Introduction
Datapath Operators
Control Structures

## Slide 3: System-Level Hierarchy
System (Top)
Complex units (cores) Simple Components
Logic Circuits
Silicon

## Slide 4: Categories of Components
Types of digital component
Datapath operators
Memory elements
Control structures
I/O cells
Tradeoff of selection
Speed
Density
Programmability
Easy of design
etc

## Slide 5: Datapath – Adder
Adder Truth Table
C A B A.B(G) A+B(P)
A B SUM CARRY
Generate Signal G(A.B): occurs when a carry output (CARRY)
is internally generated within the adder .
Propagate Signal P(A+B): when it is true, the carry in signal C is passed
to the carry output (CARRY) when C is true
A B
C
CARRY
G P
SUM
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 6: Datapath – Adder
-C
C
A
Single-bit schematic of SUM
A B C
SUM=A B C CARRY=AB+AC+BC
-A
-B
B
-A C
-A
B
-B
-A
-C
SUM
A
A
A
SUM

## Slide 7: Datapath – Adder
Single-bit schematic of CARRY
C A B
A B
CARRY
-C
-A
-B
CARRY

## Slide 8: Datapath – Adder
Optimized combinational adder schematic
Ci+1=AiBi+AiCi+BiCi Si=(Ai+Bi+Ci).Ci+1+AiBiCi
Vdd
Ai Bi Ci
Ci+1
Ci Bi Ai
Ci+1
Si
S
i
Vss

## Slide 9: Datapath – Adder
Symmetrical optimized combinational adder schematic
Ci
A
A B
A B Ci
Cout Cout
B
A B
A
B A
S
Ci
B
B
B A
Ci
A

## Slide 10: Datapath – Bit-Parallel Adder
Parallel adder implementations C<n+1>
S<n>
S<3>
B<3>
B<n> A<n>
C<n>
C<3>
B<3>
B<n> A<n>
S<n>
S<3>
C<n>
C<3>
C<n+1>
S<2>
S<1>
S<0>
A<3> B<2>
A<2> B<1>
A<1> B<0>
A<0>
Cin
A<3> B<2>
A<2> B<1>
A<1> B<0>
A<0>
S<2>
S<1>
S<0>
Cin

## Slide 11: Datapath – Bit-Parallel Adder
S<3>
S<2>
B<3>
A<3> B<2>
A<2> B<1>
C<3>
S<3>
S<2>
B<3>
B<2>
B<1>
A<3>
A<2>
C<3>
S<1>
S<0>
A<1> B<0>
A<0>
Vdd
S<1>
S<0>
B<0>
A<1>
A<0>
Subtract
A-B
If (Subtract==0)
{S=A+B;}
else
{S=A-B;}

## Slide 12: Datapath – Bit-Serial Adder
addend
110
Cout
0110
A
0 1 1 0 1
0110
augend
Result
Cin
0 1 0 0 1
B
1001011011001 0
001

## Slide 13: Datapath – Carry Look-Ahead Adder (CLA)
Objective
To avoid the linear growth of the carry delay, we use a Carry Look-Ahead Adder (CLA) in which the carries can be generated in parallel
Feature
The Carry of each bit is generated from the propagate and the generate signals as well as the input carry
The propagate and the generate signals are derived from the operand Ai and Bi by
Gi=Ai.Bi
Pi=Ai+Bi

## Slide 14: Datapath – Carry Look-Ahead Adder
Ci+1=AiBi+(Ai+Bi)Ci=Gi+PiCi C1=G0+P0C0
C2=G1+P1G0+P1P0C0 C3=G2+P2G1+P2P1G0+P2P1P0C0 C4=G3+P3G2+P3P2G1+P3P2P1G0+P3P2P1P0C0
C0
CLG1
CLG2
CLG3
CLG4
SG1
SG2
SG3
SG4
S0
S1
S2
S3
C1
C2
C3
C4
P0 G0
P0-P1 G0-G1
P0-P2 G0-G2
P0-P3
G0-G3
4-bit CLA

## Slide 15: Datapath – Carry Look-Ahead Adder
CLG1
C1
C0
G0
C0 P0
G0
P0
C0
G0
P0
P0 G0
C1

## Slide 16: Datapath – Carry Look-Ahead Adder
CLG4
G3 G2 G1 G0
C0
C4
P0 P1 P2 P3
C4=G3+P3G2+P3P2G1+P3P2P1G0+P3P2P1P0C0

## Slide 17: Datapath – Carry Look-Ahead Adder
Manchester Carry Chain
Ci+1=Gi+PiCi Gi=Ai.Bi
Pi=Ai+Bi
Introduce the carry-kill bit Ki, this term gets its name from the fact that if Ki=1, then Pi =0 and Gi=0, so that Ci+1=0; Ki=1 thus “kills” the carry-out bit.
Ci+1
Ci
Gi
Ki
Pi
Ki=Ai.Bi |  |  |  |  | 
 | Ai | Bi | Pi | Gi | Ki
 | 0 | 0 | 0 | 0 | 1
 | 0 | 1 | 1 | 0 | 0
 | 1 | 0 | 1 | 0 | 0
 | 1 | 1 | 0 | 1 | 0

## Slide 18: Datapath – Carry Look-Ahead Adder
Manchester circuit styles
Ci+1
Ci
Gi
Gi Pi
Static circuit
Pi
C
i+1
C
i
G
i
Pi
Clk
Dynamic circuit
G3
P3
G2
P2
G1
P1
G0
P0
C0
Clk
Clk
C
4
C4
C3
C2
C1
Dynamic Manchester chain

## Slide 19: Datapath – Carry Look-Ahead Adder
Extension to wide adders
If we use a brute-force approach for an 8-bit design, then the carry-out bit C8 would have a term of the form
P7 P6 P5 P4 P3 P2 P1 P0 C 0
Multilevel CLA networks can improve this problem
bit[n-1] bit[0]
n-bit adder
[i+3] [i]
4-bit CLG

## Slide 20: Datapath – Carry Look-Ahead Adder
4-bit Carry Lookahead Generator
Pi Gi
Gi+1
Pi+1
Gi+2
Pi+2
Gi+3
Pi+3
Ci+1
Ci+2
Ci+3
P[i,i+3]
G[i,i+3]
block generate
block propagate
G[i,i+3]=Gi+3+Pi+3Gi+2+Pi+3Pi+2Gi+1+Pi+3Pi+2Pi+1Gi P[i,i+3]=Pi+3Pi+2Pi+1Pi

## Slide 21: Datapath – Carry-Skip Adder
4-bit adder
ci+4
A carry-skip adder is designed to speed up a wide adder by aiding the propagation of a carry bit around a portion of the entire adder.
[i+3]
[i]
ci
k-bit adder
ci
ci+k
P[i,i+3]
ci+4+ci.P[i,i+3]
Carry-skip
Carry-skip logic
Generalization
P[i,i+3]=Pi+3Pi+2Pi+1Pi
Carry=Ci+4+P[i,i+3]Ci

## Slide 22: Datapath – Carry-Select Adder
b7 a7
b6 a6 b5 a5
4-bit adder U1 s6 s5
b4 a4
b7 a7
b6 a6 b5 a5
4-bit adder U0 s6 s5
b4 a4
c=0
c=1
c8
s7
s4
s7
s4
c8
b3 a3
b2 a2 b1 a1
4-bit adder L
b0 a0
1 0 1 0 1 0 1 0 1 0
MUX MUX MUX MUX MUX
c0
s7
s6
s5
s4
c4
c8

## Slide 23: Datapath – Conditional-Sum Adder
A0 B0
Conditional cell
S0 S1 C0 C1
A1 B1
Conditional cell
S0 S1 C0 C1
A2 B2
Conditional cell
S0 S1 C0 C1
A3 B3
Conditional cell
S0 S1 C0 C1
C0=Cin
C4
S
0
S
1
S
2
S
3

## Slide 24: Datapath – 8-bit Conditional-Sum Adder

## Slide 25: Datapath – Multipliers
a b
a b
0 0
0 1
1 0
1 1
axb
0
0
0
1
axb
Bit-level multiplier
a3 b3
Multiplication of two 4-bit words
a2 b2
a1 b1
a0 b0
a0b0
a1b0 a0b1
a2b0 a1b1 a0b2
a3b0 a2b1 a1b2 a0b3
a3b1 a2b2 a1b3
a3b2 a2b3
a3b3
p3
p2
p1
p0
p7
p6
p5
p4

## Slide 26: Datapath – Multipliers
The product axb is given by the 8-bit result p=p7p6p5p4p3p2p1p0
The ith product term pi can be expressed as
 ajbk  ci1
i j k
pi
Alternate view of multiplication process
p3
p2
p1
p0
p7
p6
p5
p4
a0)xb3
a1
a2
(a3
(axb0)2
0
(axb1)21 (axb2)22 (axb3)23
 |  | a3 | a2 | a1 | a0
 |  | b3 | b2 | b1 | b0
 |  | (a3 | a2 | a1 | a0) xb0
(a3 | (a3 a2 | a2 a1 | a1 a0)xb2 | a0)xb1 | 

## Slide 27: Datapath – Multipliers
(axb0)20
(axb1)21
(axb2)22 (axb3)23
7
6
5
4
3
2
1
0
Product register
Using a product register for multiplication

## Slide 28: Datapath – Multipliers
add (axb0) shift right
a3b0
Shift-right multiplication sequence
a2b0 a3b0
a1b0 a2b0
a0b0 a1b0
a0b0
a3b0 a2b1
a2b0 a1b1
a3b0 a2b1
a1b0 a0b1
a2b0 a1b1
a0b0
a3b1
a1b0 a0b1
a0b0
a3b1
cx
cx
add (axb1) shift right
a3b0 a2b1 a1b2
a2b0 a1b1 a0b2
a3b0 a2b1 a1b2
a1b0 a0b1
a0b0
a3b1 a2b2
cy a3b2
a2b0 a1b1 a0b2
a1b0 a0b1
a0b0
a3b1 a2b2
a3b2
cy
a3b0 a2b1 a1b2 a0b3
a2b0 a1b1 a0b2
a1b0 a0b1
a0b0
a3b1 a2b2 a1b3
a3b2 a2b3
p7 a3b3
add (axb2) shift right
add (axb3) shift right

## Slide 29: Datapath – Register-Based Multiplier
Multiplicand
Multiplier
Product register (2n)
n
clk shr
MUX
n-bit adder
n
n
n
n
0

## Slide 30
Datapath – Array Multipliers
Consider two unsigned binary integers X and Y
 i
n1 n1
i0
X 
X 2
i
 j
j0
Y 
Y 2 j
n1

n1
i  j
i0
n 1 n 1
  
i  0 j  0
n  n 1
j 0
X 2 
P  X Y 
Y 2
j
i

k  0
i  j

P 2
( X Y ) 2
k
k
i j

## Slide 31: Datapath – Array Multipliers
X3
X2
X1
X0
Y0
Y1
Y2
P0
Y3
P1
P2
P3
P4
P5
P6
P7

## Slide 32: Datapath – Array Multipliers
X3Y0
X2Y0
X1Y0
X0Y0
X3Y1
X2Y1
X1Y1
X0Y1
X3Y2
X2Y2
X1Y2
X0Y2
0
0
0
P0
P1
P2
P3
P4
P5
P7 P6
X3Y3
X2Y3
X1Y3
X0Y3
0

## Slide 33: Datapath – Booth Multiplier
Booth’s algorithm takes advantages of the fact that an adder-substractor is nearly as fast and small as a simple adder
Consider the two’s complement representation of the multiplier y

The representation can be rewritten as
yn1  2 yn2 
y  2 y  2
n1 n2
n
n
 y  2 (y  y
Extract the first two terms

The right-hand term can be used to add x to partial product
The left-hand term add 2x
 y )2 (yn3  yn2)
)2 (y
n1 n2
n1
n2
n1 n
n
y )
n2 n1
 y )  2 (y
n1 n
y  2 (y
n1
n

## Slide 34: Datapath – Booth Multiplier
y i y i  1 y i  2
Operation
0
0
0
0
1
0
0
1
1
0
0
1
0
1
0
Add 0 Add x Add x
Add 2x Sub 2x
Actions during Booth multiplication
1 0
1 1
1 1
1
0
1
Sub x Sub x Add 0
For example, x=011001 (2510), y=101110 (-1810)
1. y1y0y-1=100, so P1=P0-2x.1=11111001110
2. y3y2y1=111, so P2=P1+0.4=11111001110
3. y5y4y3=101, so P3=P2-x.16=11000111110

## Slide 35: Datapath – Booth Multiplier
Structure of a Booth multiplier
left shift 2
code
Mux sel
Adder/substractor
Pj+2
Pj+1
yi+4 yi+3 yi+2
Stage j+1
2x
x
0
left shift 2
code
Mux sel
Adder/substractor
Pj+1
Pj
yi+2
yi+1 yi
Stage j
2x
x
0

## Slide 36: Datapath – Wallace Tree Multiplier
A Wallace tree is a full adder tree structured specially for a quick addition of the partial products
Example
  A 16x16 Booth multiplier
  8 partial products are generated
  Assume that all partial products are negative so all sign extension bits are 1’s
  Sign extension correction vector is 1010101010101011
1111111111111111
11111111111111
111111111111
1111111111
11111111
111111
1111
11
1010101010101011

## Slide 37: Datapath – Wallace Tree Multiplier
Wallace tree multiplication
1st stage
4-2 compression
Partial Products
1 0 1 0 1 0 1 0 1 0 1
0 1 0 1 1
2nd stage
4-2 compression
Sign Extension Correction
Final Addition

## Slide 38: Datapath – Wallace Tree Multiplier
FA
FA
c
s
FA
FA
Inputs
FA
c
s
Cout
Cin
C
out
Cin
Inputs
4-2 compressor
Carry-save adder
Outputs
FA
c
s
FA
c
s
Outputs

## Slide 39: Datapath – Serial Multiplication
reset
serial register
X Y
1. Require MN clock cycles to produce a product for an N-bit multiplier and a M-bit multiplicand
Serial multiplier

## Slide 40: Datapath – Serial Multiplication
X
D
D
D
Serial/parallel multiplier
Y0 Y1
Y2
Y3
D
D
D
S0
S1
S2
Require M+N clock cycles to produce a product for an N-bit multiplier and a M-bit multiplicand
The critical path consists of the adders

## Slide 41: Control – FSM
output
input
clk
Mealy
Moore
output
input
clk

## Slide 42: Control – FSM
FSM design procedure
  Draw the state-transition diagram
  Check the state diagram
  Write state equations (Write HDL)
An example of state-transition diagram
R
IDLE
WAIT
EXIT
A
IDLE: (S1,S0)=(00)
WAIT: (S1,S0)=(01)
EXIT: (S1,S0)=(10)
A: car-in
C: change-ok R: rst
-A
A
-A
C
-C

## Slide 43: Control – FSM
Check the state-transition diagram
Ensure all states are represented, including the IDLE state
Check that the OR of all transitions leaving a state is TRUE. This is a simple method of determining that there is a way out of a state once entered.
Verify that the pairwise XOR of all exit transitions is TRUE. This ensures that there are not conflicting conditions that would lead to more than one exit- transition becoming active at any time.
Insert loops into any state if it is not guaranteed to otherwise change on each cycle.
Formal FSM verification method
Perform conformance checking

## Slide 44: Control – Verilog Coding Style for FSMs
module
toll_booth(clk,rst,car_in,change_ok,green);
input
clk,rst,car_in,change_ok; green;
state_reg, next_state;
output reg[1:0]
parameter IDLE = 2’b00; parameter WAIT = 2’b01; parameter EXIT = 2’b11;
always @(posedge clk or posedge rst) begin If (rst==1’b1) state_reg<=IDLE;
else state_reg<=next_state;
end
always @(state_reg or car_in or change_ok) begin
EXIT: if (car_in==1’1) begin next_state=EXIT; green=1’b1;
end else begin
next_state=IDEL; green=1’b0;
end default: begin
next_state=IDLE; green=1’b0;
end
endcase
case(state_reg):
IDLE: if (car_in==1’1) begin next_state=WAIT; green=1’b0;
end else begin
next_state=IDEL; end
WAIT: if (change==1’b1) begin next_state=EXIT; green=1’b1;
end else begin
next_state=WAIT; green=1’b0;
end
end
endmodule

## Slide 45: Control – PLA
Structure of a PLA
Minterms
AND array
OR array
A PLA represents an expression of sum-of-product (SOP)
fi   mi (a, b, c, d )
i
f1  a b  c  d  a b  c  d  a b  c  d
a b c d
f0 f1 f2 f3

## Slide 46: Control – PLA
Fuse-programmable PLA
Fuse
f0
Jin-Fu Li, EE, NCU
f1
f2
f3
a
b
c
d

## Slide 47: Control – PLA
Logic gate diagram of a PLA
f0
Jin-Fu Li, EE, NCU
f1
f2
f3
a
b
c
d